## Slide 1: Skill-Based Verification of Cyber-Physical Systems
Alexander Knüppel, Inga Jatzkowski, Marcus Nolte, Thomas Thüm, Tobias Runge, and Ina Schaefer
FASE‘2021
(accepted at FASE’20)

## Slide 2: Motivation: Cyber-Physical Systems
Automation
https://waymo.com/journey/
„I really consider autonomous driving a solved problem. […] I think we are probably less than two years away […]”
Elon Musk at Code 2016
Correct and reusable

## Slide 3: Fundamental Research Questions Remain
Ensuring functional safety/correctness is indispensable!
Non-conformance
Bugs
Why formal?
SE
But…
Scalability
Expertise
…
Q: How to integrate functional safety & provably correct function development for safe behavior into software engineering processes?

## Slide 4: Maneuver-Centric Formal Engineering Approach
Impl.
Informal Specification
Correctness Proofs
Formal Specification
Virtual Prototype
Code (Generation)
Real World
Simulation
Design
Choices
Input
Output
Customer
Analysis
Conformity
Refinement
Modelling
Correctness Proofs
Improvement
Modification
Formal
Verification
Contributions of this work:
Modelling notation for maneuvers based on Skill Graphs
Formal underpinning for correctness proofs based on Hybrid Programs
Tool support (SKEDITOR)

## Slide 5: Modelling Foundation: Skill Graphs
Hardware
Controller
Software
Source
Controller
Sink
Graph-based representation for functional dependencies (nodes: skills, edges: dependencies) (A. Reschka et al., 2015)
“What activities must the system perform to fulfill its goals?“
Skill Graph: - Used during system design - Mapping between safety goals & skills
A. Reschka, G. Bagschik, S. Ulbrich, M. Nolte and M. Maurer: „Ability and skill graphs for system modeling, online monitoring, and decision support for vehicle guidance systems“ In: 2015 IEEE Intelligent Vehicles Symposium (IV 2015), Seoul, South Korea, 2015, pp. 933-939

## Slide 6: Skill Description
Skill ID | Name |  | Requirements / Safety Obligation
… | … | … | …
S4 | “Control longitudinal dynamics“ | R1 | “Vehicle speed must not exceed 2.7 m/s“
… | … | … | …
Symbol | Description | Content
 | Defined variables or prameters | 
 | Required variables or prameters | 
 | Hybrid program | 
 | Type | action
 | Safety obligation | 
 | Precondition | 
Contract-based design methodology

## Slide 7: Hybrid Systems as a Mathematical Foundation for CPSs
Mixed modeling of continious and discrete dynamics

## Slide 8: Hybrid Programs and Differential Dynamic Logic
Differential Dynamic Logic:
Hybrid Program:
Verification by validity checking of
Seq. Compose
Nondet. Choice
Nondet. Repeat
Diff. Equation
Test Condition
Discrete
Assignment
André Platzer, “Differential dynamic logic for verifying parametric hybrid systems“, TABLEAUX 2007, Springer

## Slide 9: Example: Hybrid Program of Control Longitudinal Dynamics

## Slide 10: Verification Condition Generation
Theorem:
depends on hybrid programs defined in - skills, which can be integrated via method calling
Global contract
for all s in { }
for all s and s‘ iff s in { } and
1.
2.
3.
for all s in { }
4.
Side note: dynamic systems are modeled in action-skills and propagated to the top.

## Slide 11: Controller Assembly
Requires program independence at the moment, i.e.,
then
Follow hard shoulder may use controller implementations of child skills
Modularity + reusability + saves verification effort

## Slide 12: On Compositionanility of Skill Graphs

## Slide 13: On Compositionanility of Skill Graphs
=

## Slide 14: Tool Support: Skeditor
https://github.com/TUBS-ISF/Skeditor

## Slide 15: Reducing Verification Effort through Composition – Eval.
RQ: To what extent can skill-based compositional verification reduce
the verification effort?
=
G1
G2
G3 = G1 G2

## Slide 16: Reducing Verification Effort through Composition - Results
RQ: To what extent can skill-based compositional verification reduce
the verification effort?
Approximately 53%

## Slide 17: Summary
+
Current/Future Work:
Case Studies/modelled maneuvers
Code generation + ROS/AirSim Simulation
and more…
https://github.com/TUBS-ISF/Skeditor
a.knueppel@tu-bs.de

## Slide 18: Informal Safety Requirements for a Vehicle

## Slide 19: Feature List / Current Progress
Explicit interfaces
Implementing skills with HPs
Adopted Assume/Guarantee-Resoning (contracts)
Environmental constraints
Means for redundant modelling
Dempster-Shafer Theory for modelling sensor uncertainty
Synthesis
SPLs with Scenarios